## Slide 1
The economics of grid
defection
New england Electricity
restructuring roundTable
27 JUne 2014
Notes: Non-party strategic advisor

## Slide 2: Study background
“…one can imagine a day when battery storage technology or micro turbines could allow customers to be electric grid independent.”
- Edison Electric Institute (EEI) Disruptive Challenges report, 2013
Study Goal: Establish a fact-base for where and when solar plus battery storage hybrid power systems compete with traditional utility service
2
Study
Partners:

## Slide 3: Analytical approach
Financial Assumptions
ITC Eligibility
MACRS
Financial Analysis Model
HOMER® software
Cost Projections
Solar PV
Batteries
Inverter
Diesel Fuel*
(*Commercial Profiles Only)
2 Load
Profiles
Residential
Commercial
Hybrid System Results
Levelized Cost of Energy
Net Present Cost
kWh/yr
Replacement Costs ($/yr)
O&M ($/yr)
Emissions
Technical Specifications
Solar PV
Batteries
Inverter
Generator*
3
Notes: Simply highlight complexity of our analysis
Keep it short

## Slide 4: Geographies examined
4
Notes: Representative range of conditions that influence grid parity:
Annual solar resource potential
Range of retail electricity prices
Currently installed distributed PV
Though not a primary driver of solar-plus-battery grid parity, the degree of utility regulation also varied.
Three locations—Westchester County, NY, San Antonio, TX, and Los Angeles County, CA—are in significantly (NY and TX) or partially (CA) deregulated electricity markets.
Two locations—Honolulu, HI, and Louisville, KY—are in regulated territories.
Westchester: In metropolitan NYC area
San Antonio: is a vertically integrated municipal utility in a wholesale power region
Los Angeles: has both a municipal and investor-owned utility, but uses the wholesale market for most generation

## Slide 5: Cases modeled
Base Case
Accelerated Technology
Improvement
Demand-Side
Improvement
Combined
Improvement
PV Sunshot
Residential - $1.50/W
Commercial - $1.25/W
DOE Battery Goal
Both - $125/kWh
Efficiency Measures
Residential – 30% Reduction
Commercial – 34% Reduction
Demand Management
Residential – 2%
Commercial – None
5
Notes: Focus on what varies between the scenarios.
Lead with Base Case –
Current trajectories—declining costs and increasing adoption rates—with no radical, disruptive improvements or other developments
  stable load dynamics
  Meeting 100% of load on a typical day in a typical year
average industry accepted price forecast
ATI
The accelerated technology improvement scenario considers the impacts of sharply decreased total installed PV costs along with more aggressive battery price projections.
DSI –
The demand-side improvement scenario considers the impact of full implementation of cost-effective energy efficiency and user-controlled load flexibility to shift the load profile, especially during an allowed period of capacity shortage.
co investment in efficiency as negawatts at 2.9 cents/kWh
168 hours a year spread across many days of where active choices on load management must be made
  In winter months, when a period of cloudy weather is expected, homeowners will be able to respond by shifting when they use electricity or reducing their total consumption. This may mean waiting to wash clothes, washing dishes by hand, using lower settings on a dryer, programming appliances to run during the day, or foregoing certain energy-intensive activities like running a vacuum until the system can handle that demand.
CI
The combined improvement scenario applies the lower-cost technologies considered in the accelerated technology improvement scenario, coupled with the more efficient and flexible load profile modeled in the demand- side improvement scenario.
THOUGHTS: I figured this visual representation gets the point across and the presenter can simply talk the audience through our scenarios using this as a backup. A text heavy version is available as a hidden slide and also explains a bit more of our rationale.

## Slide 6: commercial parity timeline
6
Notes: Grid parity is already here for ALL commercial scenarios in Honolulu
Grid parity for ALL commercial combined improvement scenarios in ALL locations before 2030
ALL commercial scenarios reach parity in ALL locations by 2050
  Locales with mid to high electric prices will be competitive within 10 years
    Los Angeles, CA
    Westchester, NY
  Even locations with low electric prices will reach parity within 30 years
    Louisville, KY
    San Antonio, TX
Removing the diesel generator still results in grid parity within the next few years
  This is without demand management, efficiency, or accelerated technology
  Honolulu within two years
  Los Angeles and Westchester in the 2030s

## Slide 7: residential parity timeline
7
Notes: The combined improvement scenario reaches parity by 2020 in Honolulu, Los Angeles, and Westchester
In Honolulu, ALL scenarios reach parity by or before 2022
With demand management and efficiency only, Honolulu, Los Angeles, and Westchester reach parity prior to 2030

## Slide 8: Effects on customers and revenue In the Northeast by 2024 (Commercial)
Base Case
$0.24
Demand-side Improvement
$0.17
Accelerated Technology Improvement
$0.16
Combined Improvement
$0.12
States included in the Mid-Atlantic region for this graph: CT, MA, NJ, NY, PA, RI
8

## Slide 9: Effects on customers and revenue In the northeast by 2024 (Residential)
Base Case
$0.92
Demand-side Improvement
$0.44
Accelerated Technology Improvement
$0.47
Combined Improvement
$0.24
States included in the Mid-Atlantic region for this graph: CT, MA, NJ, NY, PA, RI
9
Notes: CI Scenario: 3.77M customers and $5.46B in sales affected

## Slide 10: The opportunity for grid connected systems
Ongoing analysis suggests grid connected solar-plus-battery systems reach parity much sooner than entirely off-grid systems
Use Case = Grid as Backup
Chart: Example - Commercial LCOE vs Grid Purchase Price
| 2014 | 2020 | 2024 | 2030 | 2040 | 2050
0% Grid Purchase | 0.80264 | 0.48716 | 0.4043 | 0.33837 | 0.31984 | 0.3064
2% Grid Purchase | 0.60668 | 0.37049 | 0.3098 | 0.26194 | 0.24992 | 0.24231
10% Grid Purchase | 0.3971 | 0.25095 | 0.21558 | 0.19166 | 0.19243 | 0.1986
25% Grid Purchase | 0.28948 | 0.20022 | 0.18151 | 0.17348 | 0.1851 | 0.19744
50% Grid Purchase | 0.23697 | 0.19264 | 0.18129 | 0.17348 | 0.1851 | 0.19744
Grid Purchase Price | 0.17 | 0.2 | 0.22 | 0.27 | 0.36 | 0.48
DRAFT - PRELIMINARY
Grid-connected systems likely have improved economics, but additional regulatory and pricing uncertainty
>15 years earlier
10

## Slide 11: Key messages
Favorable defection economics will exist for millions within a decade under conservative assumptions; potentially a lot more sooner with either technology or offer innovation
Defection is suboptimal; economics favor maintaining a grid connection absent significant pricing changes but increasing customer empowerment is inevitable
The economics favor hybrid system adoption sooner if a grid connection is maintained, with high levels of self-generation optimal
The “traditional” utility business model is broken today – utilities are making investments on behalf of customers that may not exist in the future
There is emerging value in hybrid systems; unlocking it requires new approaches to encourage a two-way transactive grid
11
Notes: Details for each point from the teaser:
For certain customers, including many customer segments in Hawaii, grid parity is here today. It will likely be here before 2030 and potentially as early as 2020 for tens of millions of commercial and residential customers in additional geographies, including New York and California. In general, grid parity arrives sooner for commercial than residential customers. Under more aggressive assumptions, such as accelerated technology improvements or investments in demand-side improvements, grid parity will arrive much sooner.
Our analysis is based on average load profiles; in each geography there will be segments of the customer base for whom the economics improve much sooner. In addition, motivating factors such as customer desires for increased power reliability and low-carbon electricity generation are driving early adopters ahead of grid parity, including with smaller grid-dependent solar-plus-battery systems that can help reduce demand charges, provide backup power, and other benefits. Still others will look at investments in solar-plus-battery systems as part of an integrated package that includes efficiency and load flexibility. This early state could accelerate the infamous utility death spiral—self-reinforcing upward rate pressures, making further self-generation or total defection economic faster.
The “old” rate recovery model, based on kWh sales, by which utilities recover costs and an allowed market return on distribution networks, central power plants, and/or transmission lines will become obsolete. This is especially profound in certain regions of the country. In the Southwest across all MWh sold by utilities, for example, our conservative base case shows solar-plus-battery systems undercutting utility retail electricity prices for the most expensive one-fifth of load served in the year 2024; under more aggressive assumptions, off-grid systems prove cheaper than all utility- sold electricity in the region just a decade out from today

## Slide 12: Issues for electricity Market restructuring
How to understand hybrid system costs and benefits, particularly given the dynamics of shifting value over time
When and how to share these emerging sources of value between customer, utility, and service/product provider
How to regulate interconnection requirements for hybrid systems
How to allocate legacy costs among retained, departing, and returning grid customers
How to manage data transparency between all players in the emerging market
12
Notes: 1 – What are the products and services that the customers and DSPP exchange
2 – What is the utility’s role in owning or providing
3 – DSPP could happen, but is that best system value?
5 – Access to the appropriate data

## Slide 13
Creating a clean, prosperous, and secure energy future
TM