## Slide 1: Project Vigilance Value of Ambri Batteries at Joint Base Cape Cod
Paul Hibbard
June 27, 2014

## Slide 2: STUDY
Functional Feasibility Study
  Funded through the InnovateMass Program of the MA Clean Energy Center
  Part of a Demonstration Pilot Project to support the development and deployment of energy storage in the Commonwealth
  FFS involves assessing the potential value of energy storage installations paired with substantial renewable generation output
  Subsequent stages: deployment of Ambri liquid metal battery systems at JBCC, other MA sites
Partners
  MA Development Finance Agency
  Ambri Inc.
  Joint Base Cape Cod
  Raytheon
  Analysis Group

## Slide 3: Functional Feasibility Study Questions
• Can Ambri’s LMB storage technology benefit the Commonwealth’s energy and environmental policy goals?
• Can installation of Ambri batteries at JBCC generate meaningful cost savings for JBCC as a retail end-use customer, and what factors affect this outcome?
• Can Ambri’s storage support more economic integration of current and/or expanded installations of renewable generation (primarily wind and solar) at JBCC (and in similar settings)?
• Can Ambri batteries enhance the resilience of power supply for JBCC’s critical mission activities if separated from the surrounding power grid? What combinations of generation and Ambri batteries would maximize resilience of critical mission activities in the most economical fashion?
• What is the value of Ambri batteries – alone or in combination with traditional and/or renewable generating assets – in regional wholesale electricity markets?

## Slide 4: Joint Base Cape Cod (JBCC)
Large Producer/Consumer
  26 GWh load (50,000 homes)
  4.5 MW avg, 6 MW peak load
  $4 million electric bill
  (Soon) over 10 MW supply/backup 7.5 MW wind, 6 MW solar, diesel
Critical Missions
  Coast Guard
  Army National Guard
  Air Force communications, intelligence, PAVE PAWS
  State & federal military/civilian opn’s, disaster response, law enforcement, municipal agencies
Cost and Policy Goals
  Lower electric costs
  Maximize value of generation
  Maintain uninterrupted power supply
  Enable operations separate from grid
  Support grid restoration

## Slide 5: Ambri
  Stackable liquid metal battery cells
  Systems about size of an 18-wheeler
  Can switch between store & discharge instantly
  Can operate as capacity/ ancillary service resource
  Can be used as energy storage (optimize value of variable output; price arbitrage)

## Slide 6
Functional Feasibility Study
Hourly load across the Base
  Aggregate hourly demand across multiple agencies
Hourly renewable generation from Base resources
  Existing wind, new wind
  New solar
Battery charge/discharge “mode”
  Storage: fully charge and then let sit? Maintain a minimum level
  Cycle: allow swing of full capability based on needs?
  Sizing: in consideration of needs and value, how big should the system be?
Value to JBCC
  Maintain specific Base “reserves?” Act as a capacity resource?
  Buy and sell energy strategically?

## Slide 7: Ambri Battery Value Streams
Battery Value | Perspective | Description | Model Approach
Retail Costs | End-use customer | Battery used to minimize all-in cost of electricity | Apply constrained optimization on battery use to minimize customer monthly bills
Critical Load; Resilience & Independence | End-use customer | Battery used to protect critical end-use operations against transmission or distribution outages, or minimize use of back-up generation | Iterative application of battery optimization to minimize hours with net positive critical load
Energy Market Arbitrage | End-use customer or wholesale market participant | Available battery storage capability used to maximize the daily/weekly value of generation in energy market | Apply constrained optimization on battery use to maximize energy market revenues (and/or minimize wholesale energy costs) considering base generation resources and load
Capacity Market Revenues | End-use customer or wholesale market participant | Battery used in power/capacity mode to gain revenues in capacity market | Calculate annual capacity market revenues under different market forecasts
Reserve Market Revenues | End-use customer or wholesale market participant | Battery used in power/capacity mode to gain revenues in reserve market | Calculate annual reserve market revenues based on historical reserve market prices
Regulation Market Revenues | End-use customer or wholesale market participant | Battery capability offered as a regulation resource | Calculate annual regulation market revenues based on average historical market prices
Deferral of Infrastructure Investment | Transmission or distribution utility | Strategic placement of battery storage to support local system reliability | Discuss qualitatively
Power System Reliability and Efficiency | Regional power system operator, wholesale customers | Integration of storage to improve the reliability and efficiency of managing power system peak loads, load-following, and reserve requirements | Discuss qualitatively
Integration of Renewable Resources | Public Policy | Facilitate greater use of low/zero carbon resources to meet state or federal policy objectives; reduce need for traditional peaking resources to balance variability | Iterative application of battery optimization to reduced use of backup generation at increasing levels of renewable integration; discuss qualitatively

## Slide 8: AG’s Renewable/Storage Optimization Model (RSOM)
Inputs
Load
  Selectable load source
  Hourly profile
Optimization Criteria
Minimize Retail Charges
  Minimize Volumetric Charges
  Minimize Demand Charges
  Minimize both
Maximize Wholesale Benefits
  Reserve Market
  Capacity Market
  Regulation Market
  Energy Market
Minimize Load (Energy Independence)
  Increase Battery Size
  Increase Generation
RSOM
Output
Optimal Hourly Battery Usage (Charge / Discharge)
Tables and Charts
  Daily/monthly/annual values for net load, battery use, and net load with storage
  Total customer monthly/ annual/lifetime cost with and without storage
  Monthly/five-day charts showing battery use, net load, and net load with storage
  Tabular comparisons of key metrics across multiple scenarios
Customer Perspectives
  End-users
  Wholesale Participants
  System operators
  Utilities
  Municipalities/Coops
Location
  Nodal, zonal, state, utility or regional price streams
Battery Specifications
  MW max output
  MWh total storage
  Round-Trip Efficiency
  Lifetime (years/cycles)
Generation Sources
  Selectable generation, expandable; hourly profile
  Behind-the-meter
Battery Optimization

## Slide 9: Full base results: 16MWh battery

## Slide 10: Full base results: 16MWh battery

## Slide 11: Critical Load Analysis
Pave Paws plus rest-of-base critical load; essentially a flat load profile
Testing two questions:
  How much more resilient would base be – and how much less back-up fuel would be needed – at different combinations of renewables and storage?
  How would batteries/renewables need to be sized to in effect go off-grid completely?
Ultimately, approach would weigh combinations of renewables, storage, back-up generation, and specific resilience objectives
Analysis demonstrates that batteries can be used to significantly increase resilience of operations, and reduce diesel (or other backup) fuel consumption

## Slide 12: Critical Load Analysis

## Slide 13: Wrap Up
Battery value depends on many factors – optimization objective, prevailing prices (wholesale/retail), surrounding infrastructure, climate (output, load), etc.
Ambri battery flexibility generates meaningful across a wide range of sizes and user objectives
Storage can harden Base operations against local power outages, and at various levels of renewable/storage combinations could dramatically reduce the use of back up fuel for critical mission operations
Storage can facilitate the integration (operationally) of higher amounts of variable renewable generation (as a local distribution issue and/or regional bulk power system issue), and enhance local and regional power system reliability
Meaningful potential for grid defection in certain circumstances through optimal sizing of flexible Ambri storage and BTM renewable capacity