## Slide 2
Restructuring Roundtable
March 24, 2017
Boston, MA
Jamie Howland Director, Climate and Energy Analysis Center

## Slide 3: Climate Goals
Scientific Consensus is generally 80% GHG emissions reductions by 2050
State-level emissions limits reflect this
Questions that need to be asked:
  How much clean energy are states on track to adopt?
  What technologies have the greatest impact?
  What emissions reductions will be achieved?

## Slide 4: The LEAP Model
Long-range Energy Alternatives Planning System
Integrated scenario-based modeling
Models entire energy system, consumption, emissions
All sectors

## Slide 5: Modeling Overview
Populate model with regional data
Build baseline
Construct policy scenarios

## Slide 6: Baseline Development
Largely based on 2016 AEO and EIA SEDS
Includes phase 2 standards for diesel trucks
Added ISO New England and NY ISO forecasts
  Continued on trendline to 2030 when needed
  Adjusted for:
    NY CES
    New Rhode Island RPS level
    Hydro import authorizations

## Slide 7: Policy Scenarios - Overview
Two policy scenarios
  Primary
    Achieves 45% emissions reduction (from 1990) by 2030
    This is the point on the straight-line path from today to 80% by 2050
  Accelerated
    50% emissions reduction by 2030
Scenario components generated using existing data, other forecasts, emerging trends

## Slide 8: Policy Scenarios
Policy levers are the same in both scenarios
  Energy Efficiency
  Vehicle Electrification
  Locational efficiency (VMT reductions)
  Fossil heating and water heating electrification
  Renewables
  Grid flexibility (storage and demand management)
  A few smaller levers – waste management, solar hot water, etc

## Slide 9: Primary Scenario
Comparison of selected policy levers

## Slide 10: Primary Scenario - Transportation
Cars and light trucks – 13% electrified by 2030
Medium-duty trucks – 2.5% electrified by 2030
Locational efficiency and VMT reductions – 5%

## Slide 11: Primary Scenario - Buildings
Electric EE– 2.5% annual savings
Gas EE – 1.4% annual savings
Oil/Propane EE – 1.2% annual savings
14% of fossil residential heating converted to heat pumps
7% fossil commercial heating converted
12% fossil residential water heating converted to heat pump

## Slide 12: Primary Scenario - Generation
Distributed PV – 10.9 GW
  Includes shared solar installations
Grid-scale PV – 5.3 GW
Onshore wind – 4.5 GW
Offshore wind – 4 GW
New hydro imports – 10 TWh / year

## Slide 13: Primary Scenario - Generation

## Slide 14: Primary Scenario - Generation

## Slide 15: Primary Scenario - Generation
Peak day analysis
  Performed for both summer and winter peak using LEAP model’s dispatch capability
  Sufficient resources in both instances
  Not a substitute for a full reliability analysis

## Slide 16: Primary Scenario – Energy Grid
Increased resources to provide flexibility
  Demand response – 2200 MW in 2030
  Active Load Management – 900 MW
  Storage – 2200 MW (current MA target is 600 MW by 2025)

## Slide 17: Modeling Results – New England

## Slide 18: Accelerated Scenario
Comparison of selected policy levers

## Slide 19: Policy Recommendations
Set stronger RPS targets
Strengthen RGGI targets
Expand carbon pricing to all sectors
Maintain or expand Energy Efficiency
Significant new efforts needed on electrification and demand management
Continue efforts to reform grid planning and modernization
Align utility incentives with policy goals

## Slide 20: Conclusions
Deep emissions results are possible with current and emerging technologies
Leading states have demonstrated good progress on many of the pieces needed
States need to do more to build full market penetration of these clean technologies