## Slide 1: Restructuring Roundtable November 15, 2013
Natural Gas & Electricity Interface Challenges
in New England
New England States Committee on Electricity

## Slide 2: New England States Committee on Electricity
Focus: Resource Adequacy, System Planning & Expansion
Resources: 6 full-time staff with diverse disciplines & experience. Consultants, enabling independent analysis & studies
More information: including all filings & comments at www.nescoe.com
New England’s Regional State Committee governed by a Board of Managers appointed by each of the New England Governors to represent the collective views of the six New England states on regional electricity matters

## Slide 3: Overview
Gas-Electric Study Phase III Report
  Phase III Study Report, detailed back-up slides, & Notice of Issuance at www.nescoe.com
Hydro-related analysis
  NESCOE Hydro Imports Whitepaper
  Hydro Imports Analysis
New England Gas-Electric Focus Group
  Purpose
  Preview of Report Approach to Solution Discussion

## Slide 4: Black & Veatch Gas-Electric Study – Purpose, Limits Study Period: 2014 - 2029 Purpose
Assess sufficiency of gas infrastructure to support power generation
Identify cost-benefit of solutions that could alleviate gas constraint
Limitations
The study is not a plan. It is based on hypothetical assumptions, any one or more of which history may prove wrong. Study results are directional and indicative. Studies are not predictions of costs that would emerge in a competitive solicitation, as the result of a negotiation, or that could be identified when a project becomes operational. The study does not pretend to have perfect foresight. It assumes policymakers will apply their judgment to the assumptions in each of the hypothetical scenarios studied, and their relation to policymakers’ beliefs about of the future. The study should be viewed accordingly, and critically.

## Slide 5: Gas-Electric Three Phase Study Overview
Phase I: Literature Review and Independent Verification
Phase II: Develop Study Scope, Approach, and Assumptions
Phase III: Perform Computer Modeling and Cost-Benefit Analyses
Phase I: Black & Veatch concluded that the New England natural gas infrastructure will be increasingly under pressure from demand growth from the power sector and that other previous efforts to study the issue had significant information gaps
In Phase II, Black & Veatch:
  Concluded that for the 14 New England sub-regions analyzed, 11 will exceed the constraint capacity level by more than 30 days/year under current infrastructure; and
  In consultation with the states, identified scenarios and sensitivities for analysis
In Phase III, Black & Veatch:
  Refined cost estimates associated with potential solutions; and
  Performed computer simulations to estimate benefits of potential solutions, the market price effects of extreme cold weather, and customer cost savings associated with various levels of gas and electricity demand

## Slide 6: Gas-Electric Study: Three Possible Futures & Solutions
Base Case Scenario 5 Solutions Studied (2, 3, 4a, 4b, 5) | High Demand Scenario 3 Solutions Studied (7, 8, 9) | Low Demand Scenario 3 Solutions Studied (12, 13, 14)
1. No New Infrastructure | 6. No New Infrastructure | 11. No New Infrastructure
2. Pipeline | 7. Pipeline | 12. LNG Peak Shaving
3. LNG Import | 8. LNG Import | 13. Imported Firm Canadian
4. Imported Canadian: a.) Economic* & b.) Firm | 9. Imported Firm Canadian | 14. Dual Fuel and Demand Response
5. Dual Fuel and Demand Response | 10. Weather (Design Day) | 15. Negative Demand Growth
Base Case
Future with higher gas demand, reduced availability of other power sources
Future with low growth in demand for power & gas



*Amount of Canadian imports varies with market prices (economic), rather than a set amount of imports equal to the maximum capacity of infrastructure (firm)

## Slide 7: Major Assumptions: Electric Power
Assumption | Base Case | High Demand | Low Demand
Load Growth | Same as the 2013 ISO-NE Capacity, Energy, Loads and Transmission 2013 – 2022 (CELT) | Same as Base Case | Limited demand growth
Energy Efficiency | As projected by the 2013 ISO-NE CELT | Energy Efficiency declines slightly from the Base Case, leading to slightly higher load growth | Completely offsets load growth
Renewable Portfolio Standards (RPS) | Each New England state meets 100% of its RPS target No stricter regulations on hydraulic fracturing; Federal GHG emissions program in 2020 | Each New England state meets 75% of its RPS target | Same as Base Case
Environmental Policy | No stricter regulations on hydraulic fracturing; Fed. GHG emissions program in 2020 | Same as Base Case | Same as Base Case
Generation Capacity | Nuclear deactivation occurs between 2032-2035; Later period capacity additions | Nuclear deactivation occurs between 2027-2030 | Same as Base Case

## Slide 8
Major Assumptions: Natural Gas
Assumption | Base Case | High Demand | Low Demand
Demand Growth | Residential, Commercial and Industrial (R-C-I) demand growth of 1.6% per year | High R-C-I demand growth, at 2.2%, with policy incentives | No demand growth
LNG Exports and Imports | Exports from Gulf Coast and West Coast; Imports - Everett MA (Distrigas) supplies will sharply decline relative to 2011 but gradually increase starting in 2019; Saint John NB Canada (Canaport) supplies will decline after firm supply contract expires in Oct 2013 | Additional 4 Bcf/d of export from the Gulf Coast and West Coast; Imports Same as Base Case | Same as Base Case
Pipeline Infrastructure | Algonquin Incremental Market (AIM) expansion in-service by 2016 | AIM in-service by 2016 Maritimes & Northeast Pipeline (M&NP) can reverse flow on an economic basis to meet demand growth from Maine and Maritimes | Same as Base Case
Natural Gas Supply | Marcellus grows at 6% per year; Eastern Canadian production increases sharply in 2014 to >350 MMcf/d and then gradually declines through 2020 | Same as Base Case | Same as Base Case

## Slide 9
High Demand Scenario
Low Demand Scenario
Scenario Analysis: High and Low Gas Demand Forecasts

## Slide 10: Black & Veatch Findings
In the absence of infrastructure or demand reduction solutions, New England will experience capacity constraints that will result in high natural gas & electric prices
Gas-supply requirements driven by episodes of extremely cold weather can be very costly & create significant reliability risks
Short- & long-term solutions are needed to relieve the natural gas market constraints under the Base Case & High Demand Scenarios
No long-term infrastructure solutions are necessary under the Low Demand Scenario; The costs of measures that could bring about the Low Demand Scenario, an additional alternative, would require study
In the absence of demand reduction solutions, a Cross-Regional Natural Gas Pipeline solution, after construction and operational costs, presents higher net economic benefits to New England consumers than do alternative long-term solutions studied

## Slide 11: Some State Observations
  A new natural gas pipeline currently in process toward operation provides significant economic benefits to electricity customers under all scenarios studied.
  An additional hypothetical pipeline provides the most substantial economic net benefits to electricity consumers of all solutions studied under the Base Case & High Demand Case.
  The actual cost to consumers for incremental hydroelectric power is currently unknown. Study assumes cost of service based pricing.
  Reducing consumers’ demand for electricity & natural gas to the extent assumed in the Low Demand Case eliminates the need for consumers to invest in infrastructure. Further analysis would be required to determine whether policies that would result in a Low Demand Scenario are cost-competitive with infrastructure investments.

## Slide 12: Hydro Solution Analysis in the Gas-Electric Study
Economic Based Imports
Assumes import levels determined by energy needs & price differentials in New England & other markets
Firm Imports
Assumes firm import levels by contract (24/7/365)
Assumes additional cost of new dam at cost of service
Enables imports even during Canadian winter peak
Both assume cost of a new 1200 MW line
Both reduce natural gas demand in New England
Both lower regional electric prices in New England
Greater reduction in gas demand during winter peaks
Greater reduction in electric prices

## Slide 13: Hydro Analysis
Hydro Whitepaper
Context for policymakers
Overview of New England’s competitive energy markets, New England & Eastern Canadian Provinces’ generation resource mixes
Power system synergies between Eastern Canadian Provinces & New England
Potential benefits & risks associated with increasing hydro imports, need for resource tracking system
Options for increasing hydro imports & implications for further consideration
Hydro Imports Analysis
High level view of economic & environmental impacts of incremental hydro imports
Assumes imports via 3 new hypothetical1200 MW lines from different points in Canada into different areas in New England
1. New Brunswick to MA
2. Quebec through NY to CT
3. Quebec to VT
Assumes 2 hydro supply outlooks
1. Base Supply Case: existing, under construction
2. Alternative Supply Case: Base Case + 5000 MW (permitted and proposed)
Cost of Service basis. Does not reflect prices that would emerge in an RFP or via negotiations

## Slide 14: NESCOE Hydro Imports Whitepaper Observation: Need to Validate Import Source To Confirm Carbon Benefits
Increased imports of Canadian power have potential to help New England states achieve carbon reduction requirements or goals
To satisfy statutory mandates and objectives, imports must be from low-carbon resource generating units and validated as such
same way New England validates clean energy attributes
Unit specific hydro validation requires
New England to make system changes
Eastern Canadian provinces to create & implement tracking & reporting systems

## Slide 15: New England Gas-Electric Focus Group
Purpose and Scope
Bridge communication gaps between electric industry, gas industry, states
Identify & evaluate challenges based on informed input from all interested stakeholders
Analyze, discuss & exchange viewpoints and facts regarding challenges and their solutions
Issue a Report – Forthcoming
  Any recommendations in the Report will be in the form of advisory recommendations for consideration by entities with responsibility/authority for implementing such solutions
  Focus Group to act by consensus and disclose views of participants who do not support consensus recommendations (if there are opposing views)

## Slide 16: Report Approach Preview – Solution Discussion
Describe agreed-upon challenges that emerged in Focus Group
List electric market-related solutions ISO-NE is on course to implement
List gas system and/or gas market-related solutions the gas industry is on course to implement
Identify potential solutions that may have appeal to some stakeholders and/or states but that require further analysis before implications can be fully understood and judgments can be formed. Identify the appropriate entity able and/or willing to develop such analysis to inform future decisions.
Identify those potential solutions about which market participants and states broadly believe there is adequate information available and about which there is no consensus
Identify those potential solutions about which there is adequate information available for decision-making and about which there is consensus. Include information about next steps, authority to implement, forward-looking process.

## Slide 17
Thanks.
More information at www.nescoe.com