## Slide 1: Reforming Retail Rates to Better Integrate DERs – The New York REV Approach
Ryan Katofsky, Advanced Energy Economy
New England Restructuring Roundtable
September 30, 2016

## Slide 2: AEE: transforming public policy to enable the rapid growth of secure, clean, and affordable energy
Leadership Council
Business Council

## Slide 3: Rate design actively being addressed in REV
Track 2 Order (May 2016)
Improve large C&I rates (already exposed to real-time energy prices).
  Credits for reliable, peak-shaving DER.
Mass-market: improve existing optional TOU rates
Prosumers: develop a “Smart Home Rate” (opt-in)
Study potential for future opt-out TVRs
Value of DER Proceeding (“LMP+D”)
Develop successor tariff to net energy metering (NEM)
More fully value DER on a time and location specific basis
Interim and full valuation methodologies under development
ALSO: Address large interconnection queue and potential revenues shift under NEM (esp. from community solar)

## Slide 4: Overview of LMP+D proceeding (15-E-0751)
Opened December 2015
Parties submitted detailed proposals in April 2016
DPS launched “informal collaborative” in May
  Meetings every two weeks
  Staff drafting full proposal due out in October 2016
Interim successor to be in place in early 2017
  Rates go into effect mid-2017
Long-term methodology to be decided by end of 2018
  Structure and scope TBD
Separate Interconnection Policy Working Group to address
  Queue management
  Allocation of interconnection costs

## Slide 5: Advanced energy community perspective
LMP+D compensation mechanism should apply…
… to all DER technologies
… to generation and load reduction
… to dispatchable and non-dispatchable resources
… to BTM, grid sided, and shared resources

## Slide 6: Summary of AEEI proposal*
Hourly variable prices ($/kWh)
  All components of LMP+D, per BCA order
  Applicable to consumption and generation
  Exports valued same as BTM DG consumption
  Retroactively calculated at bill settlement (using interval metering)
Implemented gradually
  Grandfathering of NEM for existing projects
  Retain NEM for DG customers that are “net importers”
  Becomes default for some DER customers/projects, focused on those with “significant” annual net export.
* Joint proposal of AEEI, ACE NY & NECEC, developed with help from Clean Power Research

## Slide 7: Illustration of hourly variable prices*
High price differential:
Energy costs depend on load
Capacity costs allocated by load
Hourly loss factors vary by square of load
* Only two components shown for simplicity. Actual rate would include all elements of LMP+D.

## Slide 8: Technology examples
Energy Storage
Charge at lower cost; discharge at higher cost
Narrower pricing peaks: lower energy requirements, lower capital cost
Load Management/DR
High value for peak shifting (automated DR, smart thermostats, building precooling, ice storage, etc.)
Fuel Cells
Capture highest prices through dispatch
Solar
LMP+D expected to be similar to VOS
Solar + storage looks more attractive
West-facing or tracking systems could receive higher value

## Slide 9: Core elements of latest NY DPS staff proposal for interim successor tariff
Applies to CDG, RNM and “large” C&I projects
  Grandfathering terms still TBD
  NEM-eligible technologies only
Hourly netting (requires interval metering)
BTM generation that is consumed is treated as load reduction
LMP+D rate applies to exports only
May also develop option for “buy-all, credit all” transaction
  May be advantageous for certain BTM resources

## Slide 10: Basic structure of interim LMP+D proposal from DPS staff
DER Value
Generation consumed BTM
Bulk system (“LMP”)
Distribution system (“D”)
=
+
Environmental (“E”)
Market transition pmt*
LMP+D rate (applied to exports)
Avoided retail purchases
* To ensure smooth transition and project financability. Details still TBD.
+
+
+

## Slide 11: Illustration of DPS staff interim methodology, solar example
Chart: kW
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0
Exports (LMP+E) | 0 | 0 | 0 | 0 | 9 | 22 | 33 | 45 | 54 | 57 | 59 | 60 | 59 | 57 | 54 | 45 | 35 | 22 | 9 | 0
Imports (Retail Rate) | 18 | 20 | 24 | 30 | 32 | 33 | 33 | 30 | 27 | 23 | 20 | 16 | 17 | 17 | 22 | 28 | 35 | 40 | 43 | 40 | 37 | 31 | 24 | 19
Self Consumption (Retail Rate) | 0 | 0 | 0 | 0 | 9 | 22 | 33 | 30 | 27 | 23 | 20 | 16 | 17 | 17 | 22 | 28 | 35 | 22 | 9 | 0
D Value
Distribution Peak

## Slide 12: Illustration of DPS staff interim methodology, baseload fuel cell example
Chart: kW
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0
Exports (LMP+E) | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30
Imports (Retail Rate) | 18 | 20 | 24 | 30 | 32 | 33 | 36 | 40 | 41 | 42 | 41 | 40 | 41 | 40 | 42 | 41 | 40 | 37 | 30 | 28 | 25 | 23 | 21 | 20
Self Consumption (Retail Rate) | 18 | 20 | 24 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 28 | 25 | 23 | 21 | 20
D Value
Distribution Peak
No D value if no exports during peak hours

## Slide 13: Calculation methods for latest DPS staff proposal
Bulk system (“LMP”)*
Distribution system (“D”)
Environmental (“E”)*
Market transition payment
Energy based on zonal LBMPs
Capacity based on exports coincident with ISO system peak (“ICAP tag” for top single hour)
Utility marginal capacity costs allocated to top 25 hours (distribution system peaks)
Applied to exports in top 25 hours
To be based on REC prices for Clean Energy Standard
Social Cost of Carbon as a floor price
Value TBD
Will decline in tranches based on MWs deployed
Preference is for fixed payment vs. “shock absorber”
* Adjusted for retail losses.

## Slide 14: Illustrative calculation of LMP+D value stack based on DPS staff proposal (for Central Hudson)
Chart: ¢/kWh
| NEM (residential) | PV | PV with Storage
Commodity | 7.4
Delivery | 6.1
SBC | 0.8
MFC* | 0.4
LBMP | 4.6 | 4.6
ICAP | 3.3 | 3.3
ICAPstorage | 3.2
E | 2.6 | 2.6
D | 1 | 1
Dstorage | 1.5
Market Transition Payment? | 2.5
* Merchant Function Charge
Assumes no energy price arbitrage with storage
Assumes storage enables output at nameplate capacity in peak NYISO hour
At $31/kW-yr
Assumes storage enables output at nameplate capacity in all top 25 hours
Based on PV system output in peak NYISO load hour
Based on REC price
Community Solar Project

## Slide 15: Observations
The DPS staff interim methodology, as proposed:
  Only requires interval metering (not AMI)
    Metering costs small relative to large project sizes
  Will have good temporal resolution
  Will have very limited locational differentiation
  Will not offer “avoidable D” value to BTM consumption
  Will be difficult to finance
    Discussions now focused on what components can be fixed
Elements of the New York process should be emulated
  Collaborative
  Transparent

## Slide 16: Thank You!
Ryan Katofsky
rkatofsky@aee.net
For questions about membership in AEE, please contact:
Laura Bartsch
lbartsch@aee.net