## Slide 1: T&D and Deep Mid-Century Decarbonization in New England
Presented To:
  Raab Restructuring Roundtable
Presented By:
  Jurgen Weiss
    March 13, 2020

## Slide 2: All New England States have 2050 deep decarbonization goals – three primary ways to get it done
Rhode Island (Goal)
80% below 1990 level by 2050
Vermont (Goal)
80–95% below 1990 level by 2050
New Hampshire
(Recommended Goal)
80% below 1990 level by 2050
Massachusetts (Limit)
80% below 1990 level by 2050
Maine (Goal)
80% below 1990 level by 2050
Connecticut (Limit)
80% below 2001 level by 2050
Green Electric Sector
Expand Energy Efficiency
Electrify Transportation and Buildings
(Direct/Indirect)

## Slide 3: EE+Electrification = Electricity demand in New England will likely roughly double by 2050
Efficiency Focused
Electrification Focused
Electrification and
Renewable Fuels
Transport
Residential
Commercial
Industrial
Electricity Savings
from Res & Com EE
Res & Com
Base
Direct Electrification
Transport
Res & Com
Indirect Electrification*
via Renewable Fuels
+77%
+103%
+136%
Relative to 2018:
Building Energy Efficiency | 1.5%/year | 0.7%/year | 0.7%/year
Building Electrification | All fuels: 80% Direct | All fuels: 95% Direct | Natural Gas: 50% Direct, 50% Indirect Other Fuels: 95% Direct
LDV/MDV Electrification | 90%/80% | 90%/80% | 90%/80%
HDV Electrification | 80% | 80% | 100% Indirect
Clean Electricity Generation | 95% | 95% | 100%
+40 TWh
-32 TWh
2050 New England Annual Electricity Demand (TWh)
Scenario:

## Slide 4: Higher load, lower clean capacity factors and curtailments mean a total capacity need of >200 GW
TWh
Load
Clean Energy
Storage
Gas
Curtailments
(27% of RE gen)
Monthly Supply
Hydro
Nuclear
Offshore Wind
Onshore Wind
Solar
Gas
Storage
One of several possible New England Resource Portfolios
Annual Generation
Total = 382 TWh
Installed Capacity
Total = 219 GW
  OSW/large scale solar each 10% of technical potential
  Large scale solar 7.5% of non-forested land area
  28 GW of storage primarily needed to shift excess solar generation to peak load hours
  30 GW of “gas” generation to provide seasonal flexibility – about 3% of generation. Could be renewable gas such as bio-methane or P2G
  Other portfolios possible – but unlikely to change overall conclusion materially
Note: Load includes T&D losses. Curtailments include battery losses.
35 TWh
9%
10 TWh; 3%
170 TWh
44%
14 TWh
4%
140 TWh
37%
13 TWh; 3%
Typical Winter Day
Hydro
Nuclear
Offshore Wind
Onshore Wind
Solar
Gas
Storage/Gas
Load

## Slide 5: To get there requires significantly accelerating current and currently anticipated deployments.
Cumulative Clean Energy Resources in New England
Historical
280 MW/year
2010–2018
Currently Planned
830 MW/year
2019–2030
Large-Scale Resources: | 3,500 MW/yr
Balanced Portfolio: | 5,100 MW/yr
Local Solar & Storage: | 6,600 MW/yr
Hydro
Offshore Wind
Onshore Wind
Solar
Cumulative Resources
Annual Additions
Required for 80% GHG Reductions
5,100 MW/year (Balanced Portfolio)
2019–2050

## Slide 6: Any/each of these portfolios will have important T&D system implications
We estimated a rough doubling of incremental annual national transmission investment) – largely related to connecting RE resources to grid
In New England, interconnecting 40 GW of offshore wind could be a particular challenge
Incremental U.S. National
transmission investment
NE Distribution peak impacts of electrification
Distribution investments also potentially very significant as local peaks could increase sharply
  ASHPs are particularly impactful
  Shifting to winter peak may help a bit for distribution wires

## Slide 7
  Jurgen Weiss
    Principal, Boston
    +1.617.864.7900
    Jurgen.Weiss@brattle.com
Dr. Jurgen Weiss is an energy economist with 25 years of consulting experiences. He specializes in issues broadly motivated by climate change concerns, such as renewable energy, energy efficiency, energy storage, the interaction between electricity, gas, and transportation. He spearheads Brattle’s electrification efforts. He works for electric utilities, NGOs, and government entities in North America, Europe, and the Middle East.
Dr. Weiss holds a Ph.D. in Business Economics from Harvard University, an M.B.A. from Columbia University and a B.A. from the European Partnership of Business Schools.

## Slide 8
Backup

## Slide 9: This scale of clean energy additions can be achieved if New England keeps its foot on the accelerator
  Growth rates similar to the growth of global annual renewables deployments over the past 20 years, which have averaged 11% per year for wind, 45% per year for offshore wind and 41% per year for solar PV
  But…
    Also need to scale up related infrastructure (e.g., transmission, distribution, PUC capacity, interconnection processes)
    Achieving the underlying electrification also requires acceleration (e.g., charging infrastructure, heat pump installations)
Growth Rate of Annual Capacity Additions
Offshore Wind
Onshore Wind
Solar PV
Source: IRENA, Renewable Electricity Capacity and Generation Statistics, July 2019. Note: New England (NE) bars represent the needed annual growth in the Balanced Portfolio to achieve 2050 goals.
Wind and Solar
Historical
Required to meet 2050 GHG goals

## Slide 10: Side Note: Electrification can be “direct” or “indirect”
“Direct” – use electricity directly
“Indirect” – use electricity to create drop-in fuels
Transportation
Buildings
Industry
P2G
P2L
Hydrogen via electrolysis
EVs, ASHPs, GSHPs, induction, microwave, resistance heat
Needed if bio-feed stocks are insufficient/uneconomical or if direct electrification is not possible
Long-distance air travel, shipping, and freight
High industrial heat or feedstock
Seasonal storage of surplus clean electric generation?
Uses more power than direct due to lower “well to wheels” efficiency
Total electricity demand

## Slide 11: Heating electrification will make demand grow most in the winter, more than doubling peak demand
Monthly Energy (TWh)
Monthly Peak (MW)
Space Heating
Transportation
2050 Total
Conventional Demand
Water Heating & Other
TWh
22
24
27
21
23
20
17
17
19
19
17
19
Space Heating
2050 Total
Conventional Demand
2018 Total
Water Heating & Other
2018 Total
MW
2050 Peak Demand
60,000 MW
2018 Peak Demand
25,600 MW
Any clean portfolio of resources will need to meet this new pattern of demand.
Transportation

## Slide 12: Offshore wind and solar provide the vast majority of potential clean energy resources in New England
Clean Energy Resource Technical Potential
New England
Massachusetts
Electricity demand forecast in 2050:
214–286 TWh
Electricity demand forecast in 2050:
95–140 TWh
Total potential:
953 TWh
Total potential:
3,054 TWh
New England technical potential far exceeds needs
New York also has a significant onshore wind potential
~10% of land/80% of non-forested land

## Slide 13: (Clean) costs decline and remain comparable through 2050; supply portfolio choice not mostly based on LCOE
2050 Estimated New England Resource Costs
(No tax credits, includes transmission costs to MA)

## Slide 14: 2050 Resource Portfolios Storage, gas, and hydro will play key roles in balancing system supply and demand
Winter
Spring
Summer
Fall
Note: The figures show the generation and load profiles during a high demand day of the respective season.
Hydro
Nuclear
Offshore Wind
Onshore Wind
Solar
Gas
Storage/Gas
Load
Balancing required between day and night hours using storage
Insufficient clean generation throughout the day; storage and gas required to meet load
Excess clean generation midday is stored to meet evening and early morning demand
Limited excess midday generation can be stored to meet some hours of deficiency; require gas for remaining supply
Hourly Electric Sector Load and Supply
Scenario: Balanced Portfolio